## Slide 1
EDGENTS
Coordinating Autonomous UAV Swarms via Locally-Deployed Small Language Model Agents
Devrajsinh Gohil
School of Engineering & Technology · Dhirubhai Ambani University
Supervisor: Prof. Dr. Tapas Kumar Maiti · 2026

## Slide 2
Agenda
2
1. Problem & Motivation
2. Proposed Solution — Edgents
3. System Topology
4. Complete System Architecture
5. Pilot Agent Architecture
6. Four-Layer Design
7. Safety Architecture
8. Inter-Agent Protocol
9. Experimental Setup
10. Key Results
11. Discussion & Limitations
12. Conclusion

## Slide 3
Problem Statement
3
Existing Control Paradigms Are Brittle
Pre-programmed missions fail on environmental change. Cloud-based AI creates latency, network dependency, and data-sovereignty risks.
Applying LLMs to UAVs Is Non-Trivial
• Hallucination — impossible flight commands • Grounding — live sensor data needed every cycle • Coordination — consensus on limited bandwidth • Latency — PX4 OFFBOARD 2-second keepalive timeout
The Gap We Fill
No existing system provides: ✓ Local SLM inference on commodity hardware ✓ Multi-agent coordination without cloud connectivity ✓ Deterministic safety layer decoupled from AI ✓ Open reproducible eval on PX4 SITL

## Slide 4
Proposed Solution — Edgents
4
Each drone runs a locally-deployed Small Language Model as its brain — no cloud, no internet required.
Four-Layer Architecture
Sensor → Safety → Intelligence → Execution. Deterministic safety layer cannot be overridden.
ECoT Prompting
Forces thought before action selection. Cuts format hallucination by ~75%.
9-Message Protocol
Complete mission coordination in as few as 9 envelope messages. < 1.1 KB total.
Open Evaluation Pipeline
PX4 SITL + Gazebo Harmonic + ROS 2. Fully reproducible.

## Slide 5
System Topology
5
PC-1 — Lead (10.34.211.86)
PX4 SITL Drone-0
Lead ROS 2 Stack (10 nodes)
Ollama · Qwen3.5 2B
GCS (STT / TTS / Monitor)
PC-2 — Wingman (10.34.211.15)
PX4 SITL Drone-1
Wingman ROS 2 Stack (3 nodes)
Ollama · Qwen3.5 2B
CycloneDDS WiFi ROS_DOMAIN_ID=42 /agent/lead_to_wingman /agent/wingman_to_lead /safety/event
▶
▶

## Slide 6
Complete System Architecture
Two networked PCs sharing ROS_DOMAIN_ID=42 over WiFi LAN
6
Human Operator
🎙 Microphone / STT
🔊 Speaker / TTS
🖥 Terminal Monitor
▼
PC-1 — Lead · Ubuntu 24.04 · ROS 2 Lyrical
PX4 SITL Drone-0 ns:/fmu/ key=1
Camera Plugin Gazebo
XRCE-DDS Agent udp4 :8888
lead_sensor_aggregator /drone_0/situation @ 1Hz
camera_detection_node YOLOv8-nano @ 2Hz
safety_monitor_node bat≤15% / gps<3 → RTL
lead_agent_node Qwen3.5 2B · Ollama
lead_px4_commander 10Hz OFFBOARD setpoints
stt_node + clarification_speaker
CycloneDDS WiFi /agent/ lead_to_wingman /agent/ wingman_to_lead /safety/event
▶
▶
PC-2 — Wingman · Ubuntu 24.04 · ROS 2 Lyrical
PX4 SITL Drone-1 ns:/px4_1/fmu/ key=2
Camera Plugin Gazebo
XRCE-DDS Agent udp4 :8888
wingman_sensor_aggregator /drone_1/situation @ 1Hz
wingman_agent_node Qwen3.5 2B · Ollama
wingman_px4_commander 10Hz OFFBOARD setpoints

## Slide 7
Pilot Agent Architecture
Lead Agent shown — Wingman stack is symmetric
7
Inputs
/voice_commands STT Goal
▼
/drone_0/situation 1Hz sensor string
▼
/camera_0/detections 2Hz YOLOv8-nano
▼
/agent/wingman_to_lead JSON status / ack
▼
/safety/event SafetyEvent JSON
lead_agent_node — Dual-Thread Model
ROS 2 Spin Thread rclpy.spin() Handles all callbacks
⟷
threading.Lock Shared-state protection
⟷
Daemon Thread _agent_loop() Infinite think-act
▼
context_manager.py — Prompt Builder (~960 tokens total)
[GOAL] ~20 tok
[SITUATION] ~80 tok
[MEMORY] ~100 tok
[MESSAGES] ~50 tok
[ACTIONS ≤8] ~400 tok
▼
Inference Pipeline
build_prompt()
▶
Ollama API POST /api/generate qwen3.5:2b
▶
ECoT Output {thought, tool, params}
▶
3-Attempt Retry Loop
▼
Tool Registry — 19 Tools
✈ Flight takeoff · move hover · search land · rtl
👁 Sensing get_situation scan_camera get_battery
🗄 Memory remember · recall wait mission_complete
📡 Comms message_wingman ask_human notify_human
AgentMemory SQLite ~/.ros/lead_ agent_memory.db
Outputs
/lead/approved_intent FlightIntent JSON
/agent/lead_to_wingman NL order to Wingman
/clarification_request TTS to operator
/mission_status JSON {lead, wingman}

## Slide 8
Four-Layer Hybrid Architecture
8
1 · Sensor Layer
YOLOv8-nano @ 2Hz + PX4 telemetry (position, velocity, battery, GPS) → situation string @ 1Hz injected into every inference cycle
↓
2 · Safety Layer
Deterministic. No SLM involved. battery ≤ 15% → RTL. GPS fix < 3D → RTL. VehicleCommand published ×3. Cannot be overridden.
↓
3 · Intelligence Layer
Qwen3.5 2B via Ollama. ECoT think-act loop. 19-tool registry. SQLite memory. 3-attempt retry. ~960 token context per cycle.
↓
4 · Execution Layer
FlightIntent JSON → PX4 OFFBOARD position setpoints @ 10Hz. NED frame translation. Continuous heartbeat prevents mode timeout.

## Slide 9
Intelligence Layer — Agent Loop & ECoT
9
① Sensor data arrives
ROS 2 callbacks fire: situation string, YOLO detections, peer messages, safety events all update shared state.
▼
② Prompt assembled
context_manager.build_prompt() collects 6 sections: system · goal · situation · memory · messages · actions
▼
③ Ollama HTTP POST
POST /api/generate → qwen3.5:2b (num_ctx=8192). Inference latency: 3–8 s on AMD Radeon Pro W5500.
▼
④ ECoT JSON parsed
Extracts {thought, tool, params}. Invalid JSON/tool name appended as error context; retried up to 3 times.
▼
⑤ Tool dispatched
Result logged to sliding action window (≤ 8 entries). Cycle skipped silently if all 3 attempts fail.
ECoT Output Schema (enforced by system prompt)
{ "thought": "Obstacle ahead — hover and scan.", "tool": "hover", "params": {} }
Token Budget per Inference Cycle
Context Section
Tokens
System prompt
~300
Mission goal
~20
Situation string
~80
Memory recall
~100
Agent messages
~50
Action history (≤8)
~400
Total per cycle
~950
Output (tool call JSON)
~40

## Slide 10
Tool Registry — 19 Tools per Agent
10
Flight (Both)
takeoff(altitude)
move(direction, dist)
hover()
search(duration_sec)
land()
rtl()
Sensing (Both)
get_situation()
scan_camera()
get_battery()
Memory (Both)
remember(fact)
recall(query)
wait(seconds)
mission_complete(report)
Lead-only
message_wingman(msg, type)
ask_human(question)
notify_human(message)
Wingman-only
message_lead(msg, type)
ask_lead(question)
notify_lead(message)
★ Only Lead has ask_human & notify_human — Wingman cannot contact the operator (single-command-authority principle)

## Slide 11
Safety Architecture — Deterministic, No SLM
11
• safety_monitor_node — runs independently of the agent inference loop
– Monitors BOTH drones simultaneously from PC-1
– Issues VehicleCommand NAV_CMD_RETURN_TO_LAUNCH × 3 on trigger
– Cannot be overridden by any model output — by architectural design
Condition
Threshold
Action
Battery (warn)
≤ 20%
Publish /safety/event warning
Battery (RTL)
≤ 15%
Force RTL on that drone (×3 cmd)
GPS fix type
< 3 (no 3D)
Force RTL on that drone
Result: Zero safety overrides triggered during all 8 nominal test missions

## Slide 12
Inter-Agent Communication Protocol
12
• Two dedicated ROS 2 topics bridge Lead and Wingman over CycloneDDS WiFi
– /agent/lead_to_wingman — natural language task orders from Lead
– /agent/wingman_to_lead — structured JSON status/ack from Wingman
• Strict hierarchy: Lead is the sole human interface — Wingman never contacts operator
Lead → Wingman (task)
"Fly east 50 m at 10 m altitude and report any detections found."
Wingman → Lead (status JSON)
{ "type": "status", "content": "Reached east sector. No objects detected. Hovering." }
Full mission: 9 messages total · < 1.1 KB total bandwidth

## Slide 13
Experimental Setup
13
Component
PC-1 (Lead)
PC-2 (Wingman)
Model
Dell Precision 3650 Tower
Dell Precision 3650 Tower
CPU / RAM
Intel Core i5 · 16 GB
Intel Core i5 · 16 GB
GPU
AMD Radeon Pro W5500
AMD Radeon Pro W5500
OS / ROS
Ubuntu 24.04 LTS · ROS 2 Lyrical
Ubuntu 24.04 LTS · ROS 2 Lyrical
SLM
Qwen3.5 2B via Ollama
Qwen3.5 2B via Ollama
• PX4 SITL + Gazebo Harmonic — world: baylands (PX4_GZ_WORLD=baylands)
– Drone model: x500_mono_cam (monocular camera + IMU + GPS)
– Camera bridge: ros_gz_bridge /world/baylands/...image → /camera/image_raw
• 8 independent SITL flights across 3 scenario types

## Slide 14
Test Scenarios
14
A — Nominal Coordination
Voice: "Fly 10 m north, have wingman hold position." Both drones execute without safety overrides. Measures: message count, execution time, separation distance.
B — Vision-Triggered Path Alteration
Gazebo model (person / vehicle) placed in drone camera FOV. SLM interprets YOLOv8 detection → autonomously alters search pattern. Expected response: hover + notify_human (NOT ask_human).
C — Safety Fallback Validation
Invalid command issued: "fly to altitude −500 metres". Deterministic safety_monitor_node intercepts — not the SLM. Expected: RTL issued with zero SLM involvement.

## Slide 15
Key Results
15
Mission Success Rate
75%
6 of 8 flights without manual intervention
Envelope Messages
9
6 Lead→Wingman + 3 Wingman→Lead
Total Bandwidth
< 1.1 KB
~120 B per message · 356.86 s mission
Safety Monitor
73 ticks
~0.20 Hz · zero RTL overrides triggered
Min. Separation D_min
0.02 m
At SITL init only — zero in-flight collisions
Inference Latency
3 – 8 s
15–30 TPS · 12% context window utilisation

## Slide 16
Failure Analysis
16
75% of inference cycles succeeded — tool call valid, parsed and executed
12% Format Hallucination
SLM output failed JSON validation on all 3 retry attempts. Cycle skipped silently — flight continues on last known setpoint.
8% Physical Hallucination
Valid tool name, impossible parameter (e.g. distance: 0 m). Commander receives no-op, publishes warning, heartbeat continues.
5% Coordination Failure
Lead emitted mission_complete before Wingman ACK received. Premature termination — Wingman left hovering autonomously.

## Slide 17
Discussion
17
Hybrid Architecture
Strict Safety–Intelligence separation was the critical enabler. Dangerous commands intercepted before reaching the flight stack. Mirrors established avionics safety patterns.
ECoT Prompting
Mandatory thought field forces self-supervision before action. Removing it raises format hallucination from <5% to >20%. Logically inconsistent actions self-corrected in reasoning trace.
Bandwidth Trade-off
9 natural-language messages vs. continuous binary control streams. Communication overhead: ~30–72 s (~8–20% of mission time). Acceptable for most swarm applications.

## Slide 18
Limitations & Future Work
18
SITL Fidelity
D_min = 0.02 m artefact from shared virtual origin at init. Physical hardware tests required.
Scalability (N > 2)
Architecture hard-coded for exactly 2 drones. Needs dynamic roster + per-agent context isolation.
Model Size
Qwen3.5 2B is minimum viable. 7B/14B may improve MSR at cost of higher latency.
Persistent Memory
SQLite has no automated expiry. Stale context risk in long-duration missions.

## Slide 19
Conclusion
19
• Edgents proves that a 2B-parameter SLM on commodity hardware can:
– Accept spoken natural-language mission goals via STT
– Coordinate two autonomous drones through a sparse 9-message protocol
– Maintain safety via a deterministic layer the SLM cannot override
– Achieve 75% mission success over 8 SITL flights
– Operate with < 1.1 KB inter-agent bandwidth per mission
• Key insight: the hybrid architecture is the enabling principle — not raw model capability
• Opens a path to resilient, privacy-preserving, network-independent drone coordination
Thank you — Questions welcome 202511004@dau.ac.in · Dhirubhai Ambani University